Assignment 0
Part 2 Write Up

## Overview:
1. The ‘prog-add.c’ takes input from user via scanf.
2. add(int64_t, int64_t) function is called whoich is defined in add.asm file.

3. Add function working:
- Addition of the 2 parameters present in rdi and rsi register.
- Checks if the number is negative using ‘test’ function.
- If negative then negates rax using ‘neg’ function, and sets r11 flag to 1.
- Calls the printDigit function to print the sum in rax register.
- Exits using sys_exit system call.
4. PrintDigit working:
- Initiates counters, ‘0’ characters and 10 in scratch registers.
- push_while loop pushes the digits of the sum from least to most significant bit.
- If r11 flag is 1, then prints a negative sign.
- pop_while loop pops the digits and adds 48 to convert to ascii and then print using sys_write system call.
- Finally a newline character is printed and returned
5. Control is returned to ‘prog-add.c’ which exits with status 0.

## Steps of compilation

### Pre-processing:
$ gcc -no-pie -g -Wall prog-add.o add.o -o main
- “-E” flag to stop the compilation at pre-processing
- Removes the comments.
- Includes the code of header files which have function and macro definitions. (Here <stdio.h>)
- Replaces macros by their value.

### Compiling:
$ gcc -S prog-add.i -o prog-add.s
- “-S” to stop the compilation at compiling.
- Uses the pre-processed code to generate IR (Intermediate Representation) Code I.e the assembly code.

### Assembling:
Assembling the assembled c code:
$ gcc -c prog-add.s -o prog-add.o
- “-c” to stop the compilation at assembling.
- Converts the IR code to object code which is in machine language.

Assembling the add function Assembly Code:
$ nasm -felf64 add.asm
- Nasm is the assembler used to assemble assembly code.
- ‘-f’ flag specifies the configuration to be used.
- ‘-elf64’ specifies to execute the assembling in 64bit format.
- Produces a .o file with converted object code.

### Linking:
Compile c code and link with assembly code:
      $ gcc -no-pie -g -Wall prog-add.c add.o -o main.
Links multiple source files (object codes) together to form one single executable file which can be run by “./<name_of_executable>”.
- ‘-no-pie’ flag is used to suppress the warning created when reference to a variable is changed.
- ‘-g’ flag is used to run in debug mode (gdb).
- ’ -Wall’ flag shows all the compiler warnings if any.
- ‘-o’ flag to specify output file name.